## Slide 1: Truck Simulator
By,
Jonathan Jenkins
ME 5751: Robotic Motion Planning Dec 8, 2022

## Slide 2: Objective
Develop a Truck Based motion planner
Construct a collision - free path between some initial position to some goal position.
Implement Truck kinematics to constrain the simulated robot motion

## Slide 3: Requirements
Rubric 1: Potential map generation
Rubric 2: Path planner
Rubric 3: P - controller
Rubric 4: Wheel Kinematics of a truck

## Slide 4: Potential Map Generation
Takes 500*500-pixel map and converts it into a 500*500 matrix map
Using a function to identify empty spaces ( white) and occupied spaces (black).

## Slide 5: Potential Map Generation
Assign a risk value to all empty spaces.
Spaces closer to an occupied space will be given a higher risk, While spaces that are farther away are assigned a lower risk.
  Black – 1000
  Safety-zone – 850
  Unoccupied space 800---- 0

## Slide 6: Path Generation
A planner decides what grids should the robot move to reach the desired location
A* Algorithm
  combines Breadth First Search (BFS) and Dijkstra algorithm
  BFS algorithm assigns each grid a value corresponding to the distance from the starting position
  Dijkstra’s algorithm assigns each grid a value corresponding to the distance from the goal position

## Slide 7: Dual Search A* Algorithm
The A* algorithm uses both BFS and Dijkstra’s algorithm to find an efficient path between the start and the goal . A* algorithm priority search allows it to find a path without the need to search the entire map.
We implement a dual A* search starting from both the goal position and the start position simultaneously.
With a dual search the program can scan from two location congruently, ideally allowing the program to locate a final path faster.

## Slide 8: A* Algorithm Improvements
56% Iterations Reduction
Dual Search
Single Search

## Slide 9: Point Tracking
Converting our found path to robot waypoints.
Point tracking
  We discretize the paths into a set of waypoints (positions)
  Assign a direction value to each waypoint
  Reduce the number of waypoints in a path to maximize efficiency

## Slide 10: Point tracking
Create a list of waypoints from a fraction of points in the found path
Each Waypoint is assigned a theta value based on the travel direction from the previous waypoint

## Slide 11: Point tracking
Further reduction of waypoints based on linear distance and theta value.
Sharp turns will have more waypoints for higher resolution
Strait paths will have less points

## Slide 12: Controller
Proportional control (P control) is a type of linear feedback control system in which a correction is applied to the controlled variable.
  Error (e) : the difference between the desired value and the measured value.
  Proportional gain (k) : the size of the correction that will be implemented
A P-Control was used to adjust the robot’s linear and angular velocity in order to control it to reach a desired point (goal point)

## Slide 13: Truck Dynamics
A truck has certain kinematic constraints . Based on the vehicle design and limitations we need to implement limitations to allow for accurate simulation.
  Car width : 2L = 16
  Car axile distance : d = 20
  Wheel diameter : r = 3
  Steering angle : b < 40 Degrees
  Wheel speed : rho < 20 rad/s

## Slide 14: Truck Dynamics
Incorporating the desired velocity and rotation from the p-controller and limiting the output based on the truck kinematics
  P Controller + Truck Kinematics
  Limit outputs based on known constraints
  Outputs the final vehicle linear and angular velocity that will be executed.

## Slide 15: Demonstration

## Slide 16: Link To Online Video
https://youtu.be/2k3NQvptN9E